## Slide 1
GIS ANALYTICAL TOOLS
Concept for LUPMIS2
Overlays · Zonal Statistics · Network Analysis · Interpolation · Hydrology
Presented to the Technical Working Group · LUSPA · July 2026

## Slide 2
What LUSPA asked for
Five families of analytical tools — mainly raster, but also applying to existing vector data
Overlays — combine layers to find where they intersect, differ or coincide (parcels inside a flood zone).
Zonal Statistics — summarise values within each zone (mean slope or elevation per parcel).
Network Analysis — routing and accessibility over the road network.
Interpolation — build a continuous surface from scattered sample points.
Hydrology — derive drainage and simulate flooding from a digital elevation model.
The request is raster-oriented — but the outputs matter most when combined with the parcels, zones and roads already in LUPMIS2.

## Slide 3
Where LUPMIS2 stands today
A strong vector foundation — two clear gaps
Already in place
• Map, drawing and editing (OpenLayers + ol-ext)
• Parcels, zones and OSM roads in PostGIS
• Local SQLite cache + offline tiles
• Measurement, buffer and area analysis
• GIS import / export and staged upload
• Elevation contours from OpenTopography
The gaps
• Raster handling — no GeoTIFF display and no
raster analysis
• Geoprocessing — no overlay, zonal, routing,
interpolation or hydrology operations
Both gaps are addressed by this concept. Stage 1 has already been built and is working — see slide 11.

## Slide 4
Recommended architecture — hybrid
Light vector work in the browser (offline-capable); heavy raster and network analysis on the server

## Slide 5
The five tool families
Where each runs, what drives it, and the burden it carries
Tool family | Data | Runs on | Engine | Stage | Complexity
Overlays | Vector (+ raster) | Client + Server | Turf.js / PostGIS | Stage 1 | Low
Zonal Statistics | Raster × Vector | Server | PostGIS Raster | Stage 1 | Low
Interpolation | Points → Raster | Server | GDAL / SAGA | Stage 2 | Medium
Network Analysis | Vector (roads) | Server | pgRouting | Stage 2 | Medium
Hydrology / Flood | Raster (DEM) | Server | WhiteboxTools / GRASS | Stage 3 | High
“Complexity” is the build-and-maintain burden for a small technical team — the deciding factor in the staging.
The two Stage 1 families are already built. Stages 2 and 3 add server-side engines — pgRouting, GDAL/SAGA, then WhiteboxTools — in that order of difficulty.

## Slide 6
Where the data comes from
Five sources, one object store, one map
Officer GeoTIFF upload
Rasters uploaded through the staged-upload pipeline, converted to COG on the server.
WMS / WFS services
External live layers — already supported today.
In-house PostGIS
Parcels, zones, roads — plus elevation contours from OpenTopography.
Google Earth Engine
Global catalogue that can also compute. Licensing to confirm for government use.
Digital Earth Africa
Open, Africa-focused. Already used for slope; exports COGs directly.
Survey / GPS points
Sample values feeding interpolation.
LUSPA MinIO object store — bucket “raster-objects”: live over HTTPS with anonymous read, byte-range requests and CORS. Verified for COG streaming.

## Slide 9
Terrain we already own
The DEM prerequisite can be met in-house — no external dependency
Already in PostGIS. Elevation contours (spatial.be_contours_hillshade) generated with gdal_contour at 10–20 m intervals from OpenTopography’s SRTM 30 m / Copernicus 30 m DEM — district-scoped and spatially indexed.
Interpolate a district DEM from them. That DEM is what slope, elevation zonal statistics and screening-level hydrology depend on.
Works offline. Sourced entirely in-house, so a first terrain analysis needs no external service at all.
Cloud sources then enrich it. Earth Engine and DE Africa add rainfall, surface-water history, land cover and radar flood extents on top.
Practical consequence: Stage 3 hydrology is not blocked waiting for a data-sharing agreement.

## Slide 10
Staged delivery
Each stage is useful on its own; nothing depends on the hardest tier being built first
Stage | Scope | Builds on | Dependencies | Maintenance
Stage 1 | Vector overlays; zonal statistics; raster display (COG + WMS) | PostGIS, OpenLayers, Turf.js | Raster display | Low
Stage 2 | Interpolation; network analysis; GeoTIFF upload pipeline; cloud-catalogue ingestion | PostGIS Raster, pgRouting, GDAL | Routable road topology; object storage | Medium
Stage 3 | Hydrology: flow / watershed products; screening-level flood indication | WhiteboxTools / GRASS, quality DEM | DEM quality; specialist skills; compute | High
If effort is constrained, Stages 1–2 already deliver the majority of day-to-day planning value.
Stage 1 is delivered. The decisions on slide 14 determine how quickly Stage 2 can start — and whether Stage 3 is built in-house or outsourced.

## Slide 11
Stage 1 — already built and working
Not a plan — this is in the application today
✓ Vector overlays
Intersect, Clip, Difference and Union / Dissolve — computed in the browser, so they work offline.
✓ Zonal statistics
Count, sum, mean, minimum, maximum and total area per zone, by centroid or any-overlap.
✓ Raster display
Cloud-Optimized GeoTIFF streaming plus the existing WMS support. Opened by URL.
Analysis panel with scoping
Run on the whole layer, the current map view, a hand-picked selection — or on exactly what a drawn Circle / Area caught.
Built for real data volumes
43 zones against 25,004 parcels completes in about 0.1 seconds, using bounding-box pre-filtering.

## Slide 12
What a small team can sustain
An honest split — this is the crux of the staging
Sustainable
Stages 1 and 2 extend the current stack: PostGIS spatial SQL, pgRouting, GDAL and Turf.js.
Standard, stable skills — no dedicated GIS-analysis specialist needed to keep them running.
Possible, but demanding
Full raster pipelines and hydrodynamic flood modelling need specialist hydrology / GIS expertise, careful DEM preparation and calibration, and heavier compute.
Closer to a modelling project than a feature.
Recommendation
Build the derived-terrain and screening-level products in-app. Treat detailed flood modelling as a specialist activity, with LUPMIS2 as the platform that displays and disseminates its results.
Using Earth Engine or DE Africa for data — and some of the computation — removes much of the storage and compute load from the LUSPA server.

## Slide 13
Alignment with the ToR and Functional Specifications
ToR §2.4.2 Spatial Analysis and Mapping · FS §2 Mapping & Spatial Analysis
Requirement | Source | Covered by | Coverage
Advanced spatial analysis — patterns, relationships, trends | ToR 2.4.2b | Overlays, Zonal Statistics, Network Analysis, Interpolation | Full
Heatmaps / density maps | ToR 2.4.2b | Interpolation surfaces, styled thematically | Full
Buffering, overlay, proximity | FS §2 | Buffering (existing) + Overlays + Network Analysis | Full
Summaries and statistics (mean, median, variance …) | FS §2 | Zonal Statistics + attribute aggregation | Full
Connect to Google Earth Engine, ERA5, WorldPop | FS §2 | Earth Engine integration — and DE Africa | Full
Terrain analysis — slope, aspect, hillshade | FS §3 | In-house contours → DEM, plus Hydrology | Full
Thematic mapping; raster processing | FS §2 / §3 | Basic today; richer styling and processing planned | Partial
3D visualisation; AI / ML capabilities | FS §2 | Separate workstreams — FS itself leaves AI/ML for LUSPA to define | Out of scope
Every analysis capability the ToR and Functional Specifications explicitly ask for is covered. The two exclusions are deliberate, separately-scoped workstreams — not gaps in this concept.

## Slide 14
Decisions we need from the TWG
Five questions that shape delivery
1. Server-side geoprocessing. Can PostGIS Raster, pgRouting and GDAL be added to the API server?
2. Cloud platform. Is Earth Engine cleared for operational government use — or do we standardise on DE Africa, which carries no such question?
3. Authoritative DEM. Which elevation source and licence governs terrain and hydrology work?
4. Flood ambition. Is a screening-level indication inside LUPMIS2 sufficient, or is calibrated hydrodynamic modelling required?
5. External services. Which WMS / WFS layers should be integrated first?
Also for action: MinIO access keys are currently hardcoded in the integration scripts and should be moved to environment variables.

## Slide 15
In short
A hybrid design: light analysis in the browser, heavy analysis on the server.
Delivered in three stages — each independently useful, sequenced by what a small team can maintain.
Stage 1 is already built: overlays, zonal statistics and COG raster display are working today.
The terrain data needed for Stage 3 is already in-house; cloud catalogues enrich rather than gate it.
Detailed flood modelling stays a specialist activity — LUPMIS2 displays its results.
Thank you — questions welcome